## Slide 1
MU3: Properties on Griffiths Street - Managed Retreat. Relocate properties from Griffiths Street
MU3: Emu Beach Holiday Park - Managed Retreat of assets in the southern portion
MU3: Emu Beach Holiday Park – Upgrade of groyne field
MU3: Emu Beach Holiday Park - Upgrade existing protection structure (western extent)
MU4: Foreshore Reserve - Seagrass replenishment program to be continued
MU4: Foreshore Reserve - Revetment be upgraded (eastern extent) and redevelopment of foreshore park and removal of sandbag revetments
MU5: Eastern Oyster Harbour Beach - Sand nourishment
Emu Beach
Foreshore Management Plan
recommendation 14
recommendation 15-17, 19
recommendation 20
CHRMAP Recommendations

## Slide 2: Proposed Coastal Infrastructure
MU4 Hazard Map with existing structures (top) without existing structures (bottom)
The first row of houses on Griffiths St are the most vulnerable private property to coastal inundation as they are located furthest seaward without any ‘hard’ coastal protection
The rock revetment seawall in in MU4 is critical to the preservation of important coastal assets, it is nearing its design life and may pose risk for public access
The shared path and foreshore reserve fronting Big4 is at risk from inundation due to an eroded upper beach
The trial GSC groyne structures have been shown to retain sediment on the west and due to their reduced length and lowered profile allow sediment to bypass. They are currently at the end of their initial trial life
Eastern section of Oyster Harbour Beach is prone to seasonal erosion reducing recreational amenity due to the point of no useable beach.
Coastal protection is to have a design life of at least 50 years (may be staged) and to be developed in conjunction with key stakeholders to provide high quality community amenity
Avoid locating facilities too close to an eroding shoreline or on the eroding side of a groyne where there is a risk of damage or loss
Stabilise adjacent exposed sand through planting or mulching the surface
Emu Beach
Foreshore Management Plan
Design Requirements and Key Principles
Notes: These are key design constraints and key principles that form the Basis of Design for the coastal protection works
They have come from CHRMAP Implementation Plan, WAPC policies, the result of stakeholder consultation as well as recent condition assessments which will append the FMP and are recommended to be ongoing

## Slide 3: 1. Determine the water level range for the site – including wave setup and sea level rise 2. Determine the design storm wave heights 3. Select minimum stable armour size for the design waves 4. Determine run-up as well as permitted overtopping to decide the crest elevation 5. Aim to protect and maintain coastal foreshore reserves, integration of coastal/marine planning and land use planning, protection of significant views and vistas, protection of significant natural landscapes and protection of significant indigenous and cultural heritage 6. Design scour level, adequate toe protection and founding 7. Design suitably sized, sorted and compacted filter layer as well as geotextile layers and fill material and compaction for new designs or expanded seawall sections 8. Confirm extent, spacing and alignment of rock structures (groynes and revetment)
Proposed Coastal Infrastructure
Emu Beach
Foreshore Management Plan
Design Process

## Slide 4
Groyne field to be upgraded:
  Additional groyne to be added (following detailed design)
  Length, width, height and spacing of groynes to be finalised (following detailed design)
  All groynes to be built from suitably sized granite
  Beach nourishment to infill between western groyne and rock revetment. Beach will be graded and profiled over the dry beach to match natural profile.
Triggered beach nourishment:
  Eastern section of Oyster Harbour
Opportunistic beach nourishment:
  upper beach between the western groyne and rock revetment
  the western lee of the detached breakwater
Proposed Adaptation Concept - Short Term (0-10 years)
Emu Beach
Foreshore Management Plan

## Slide 5
Current and proposed alignment
Rock revetment to be upgrade based on a Trigger Value:
  rating of ‘Very Poor’ resulting from standardised assessment
  Greater than three (3) overtopping events of the structure within a 12-month period
  A condition assessment of structures to be undertaken every 3 years
Alignment to match pre-structures natural beach
Rock to be local sourced granite
Slope to be decreased to 1V:3H minimum
Landscaping to discourage public access to the coastal protection structures
Proposed Adaptation Concept - Triggered
Emu Beach
Foreshore Management Plan

## Slide 6
Managed retreat of assets based on a Trigger Value
Proposed Adaptation Concept - Triggered
Emu Beach
Foreshore Management Plan
Emu Beach Holiday Park (southern assets):
Relocation of assets when HSD is less than 40m from lease boundary
The City has been working with the leaseholder (Big4) to plan for staged retreat of assets within the southern portion of the site as well as commence discussions around the re-alignment of the current lease boundary
Griffiths St:
Relocation of properties when Horizontal Shoreline Datum (HSD) is less than 40m from Griffiths Street